## Slide 1
Network Professional
BEGINNER TO EXPERT GUARANTEED
ACCESS MORE COURSES PLAYLIST LINK IN DESCRIPTION

## Slide 2
Networking Basics
Network Types
Network Topologies
Network Devices
Transmission Modes
Digital Transmission
Transmission Media
How Internet Works
IP Addressing IPv4 & IPv6
Subnet Mask, MAC, DHCP & DNS
WLAN & WPAN Networks
OSI Model
TCP/IP Model
TCP & UDP
ARP & RARP
CSMA/CA & CSMA/CD
Proxy & VPN
Server & Datacenter
Topics going to Cover

## Slide 3
Topics going to Cover
19. Network Security
20. NAS & NAT
21. RAID (Redundant Array of Independent Disk)
22. Sharing Folder in Network
23. TELNET in Network
24. Remote Desktop Connection
25. Windows Remote Assistance
26. FTP in Network
27. Configuring Network
28. Configuring Router
29. Protocols You need to know
30. Networking Commands you must know

## Slide 4: 1.
Networking Basics

## Slide 5
Network?
A network consists of two or more computers that are linked in order to share resources, exchange files or communication.The computers on a network may be linked through cables, telephone lines, radio waves, satellites, or infrared light beams.

## Slide 6
Networking?
Networking, also known as computer networking, is the practice of transporting and exchanging data or information & having communication between connected nodes over a shared medium.

## Slide 7
Internet?
Collection of Networks is Internet. The first workable prototype of the Internet came in the late 1960s with the creation of ARPANET, or the Advanced Research Projects Agency Network. Which was designed for US defence. Later Sir Tim berners lee introduced WWW cocept and starts web.

## Slide 8
Message or Token?
When one of the systems on the network has the "token," it can send information to the other computers. Since there is only one token for each token-ring network, only one computer can send data at a time. It verify that the target reciever is present or not before sending the data from sender.

## Slide 9
Peer to Peer Model
Architecture

## Slide 10
Client-Server Model
Architecture

## Slide 11
Peer to Peer VS Client-Server Model

## Slide 13: 2.
Network Types

## Slide 14
Basic Types of Networks
Personal Area Network (PAN)
Local Area Network (LAN)
Wide Area Network (WAN)
Wireless Local Area Network (WLAN)
Campus Area Network (CAN)
Metropolitan Area Network (MAN)
Storage Area Network (SAN)
Enterprise Private Network (EPN)
Virtual Private Network (VPN)

## Slide 15
1. Personal Area Network (PAN)
PAN is the most basic type of computer network. This network is restrained to a single person, PAN offers a network range of 10 meters from a person to the device providing communication.

## Slide 16
2. Local Area Network (LAN)
LAN is the most frequently used network. A LAN is a computer network that connects computers together through a common communication path, contained within a limited area, A LAN encompasses two or more computers connected over a server. The two important technologies involved in this network are Ethernet and Wi-fi.

## Slide 17
3. Wide Area Network (WAN)
WAN is a type of computer network that connects computers over a large geographical distance through a shared communication path. It is not restrained to a single location but extends over many locations. WAN can also be defined as a group of local area networks that communicate with each other.
WAN

## Slide 18
4. Wireless Local Area Network (WLAN)
WLAN is a type of computer network that acts as a local area network but makes use of wireless network technology like Wi-Fi. This network doesn’t allow devices communicating over physical cables like in LAN, but allows devices to communicate wirelessly.

## Slide 19
5. Campus Area Network (CAN)
CAN is bigger than a LAN but smaller than a MAN. This is a type of computer network which is usually used in places like a school or college. This network covers a limited geographical area that is, it spreads across several buildings within the campus.

## Slide 20
6. Metropolitan Area Network (MAN)
A MAN is larger than a LAN but smaller than a WAN. This is the type of computer network that connects computers over a geographical distance through a shared communication path over a city, town or metropolitan area.

## Slide 21
7. Storage Area Network (SAN)
SAN is an abbreviation of the Storage Area Network. Storage Area Network is a dedicated, specialized, and high-speed network which provides block-level data storage. It delivers the shared pool of storage devices to more than one server.

## Slide 22
8. Enterprises Private Network (EPN)
EPN is a type of computer network mostly used by businesses that want a secure connection over various locations to share computer resources.

## Slide 23
9. Virtual Private Network (VPN)
A virtual private network extends a private network across a public network and enables users to send and receive data across shared or public networks as if their computing devices were directly connected to the private network.

## Slide 24: 3.
Network Topologies

## Slide 25
Basic Types of Network Topologies
Bus Topology
Star Topology
Ring Topology
Tree Topology
Mesh Topology
Hybrid Topology
Daisy Chain Topology

## Slide 26
1. Bus Topology
The bus topology is designed in such a way that all the stations are connected through a single cable known as a backbone cable. The backbone cable is considered as a "single lane" through which the message is broadcast to all the stations.

## Slide 27
2. Star Topology
Star topology is an arrangement of the network in which every node is connected to the central hub, switch or a central computer. The central computer is known as a server, and the peripheral devices attached to the server are known as clients.

## Slide 28
3. Ring Topology
Ring topology is like a bus topology, but with connected ends. The node that receives the message from the previous computer will retransmit to the next node.
The data flows in a single loop continuously known as an endless loop. The most common access method of the ring topology is token passing.

## Slide 29
4. Tree Topology
Tree topology combines the characteristics of bus topology and star topology. A tree topology is a type of structure in which all the computers are connected with each other in hierarchical fashion. If the central hub gets fails the entire system fails.

## Slide 30
5. Mesh Topology
In this type of topology, a host is connected to one or multiple hosts.This topology has hosts in point-to-point connection with every other host or may also have hosts which are in point-to-point connection to few hosts only.
Two types Full Mesh Topology & Partially Mesh.

## Slide 31
6. Hybrid Topology
The combination of various different topologies is known as Hybrid topology. When two or more different topologies are combined together is termed as Hybrid topology and if similar topologies are connected with each other will not result in Hybrid topology.

## Slide 32
7. Daisy Chain Topology
This topology connects all the hosts in a linear fashion. Similar to Ring topology, all hosts are connected to two hosts only, except the end hosts.Means, if the end hosts in daisy chain are connected then it represents Ring topology.

## Slide 33: 4.
Network Devices

## Slide 34
Basic Types of Network Devices
NIC Card
Hub
Switch
Router
Repeater
Modem
Bridge
Gateway
Access Point
Server

## Slide 35
1. NIC Card
NIC or network interface card is a network adapter that is used to connect the computer to the network.bIt has a unique id that is written on the chip, and it has a connector to connect the cable to it. The cable acts as an interface between the computer and router.

## Slide 36
Wireless NIC
Wired NIC
NIC Card

## Slide 37
2. Hub
A hub is basically a multiport repeater. A hub connects multiple wires coming from different branches, for example, the connector in star topology which connects different stations. Hubs cannot filter data, so data packets are sent to all connected devices. they do not have the intelligence to find out the best path for data packets which leads to inefficiencies and wastage.

## Slide 38
Hub

## Slide 39
3. Switch
A switch is a hardware device that connects multiple devices on a computer network. A Switch contains more advanced features than Hub. A Switch does not broadcast the message to the entire network like Hub. It determines the device to whom the message is to be transmitted. Therefore, we can say that switch provides a direct connection between the source and destination. It increases the speed of the network.

## Slide 40
Switch

## Slide 41
4. Router
A router is a device like a switch that routes data packets based on their IP addresses. It is used to receive, analyze and forward the incoming packets to another network. A router forwards the packet based on the information available in the routing table.

## Slide 42
Router

## Slide 43
5. Repeater
Its job is to regenerate the signal over the same network before the signal becomes too weak or corrupted so as to extend the length to which the signal can be transmitted over the same network. An important point to be noted about repeaters is that they do not amplify the signal. When the signal becomes weak, they copy the signal bit by bit and regenerate it at the original strength.

## Slide 44
Repeater

## Slide 45
6. Modem
It stands for Modulator/Demodulator. It converts the digital data into an analog signal over the telephone lines. It allows the computer to connect to the internet over the existing telephone line.
Standard PC modem or Dial-up modem
Cellular Modem
Cable modem

## Slide 46
Modem

## Slide 47
7. Bridge
A bridge is a repeater, with add on the functionality of filtering content by reading the MAC addresses of source and destination. It is also used for interconnecting two LANs working on the same protocol. It has a single input and single output port.

## Slide 48
Bridge

## Slide 49
Types of Bridges
Transparent Bridge :-
Translational Bridge :-
Source Routing Bridge :-
Remote type Bridge :-
These are the bridge in which the stations are completely unaware of the bridge’s existence
A type of bridge that interconnects two different types of LAN protocols, such as Ethernet and Token Ring.
A type of bridge that interconnects 2 different types of LAN protocols, such as Ethernet and Token Ring.
A device that connects two LAN segments together that are in geographically dispersed locations. It connects LANs via a WAN.

## Slide 50
8. Gateway
A gateway is a network node that forms a passage between two networks operating with different transmission protocols.
The gateway converts information, data or other communications from one protocol or format to another. A router may perform some of the functions of a gateway.

## Slide 51
Gateway

## Slide 52
9. Access Point
An access point is a device that creates a wireless local area network, or WLAN, usually in an office or large building. An access point connects to a wired router, switch, or hub via an Ethernet cable and device that allows other Wi-Fi devices to connect to a wired network.

## Slide 53
Access Point

## Slide 54
10. Server
A server is a computer or system that provides resources, data, services, or programs to other computers, known as clients, over a network. In theory, whenever computers share resources with client machines they are considered servers. Typical servers are database servers, file servers, mail servers, print servers, web servers, game servers, and application servers.

## Slide 55
Server

## Slide 56: 5.
Transmission Modes

## Slide 57
Transmission Mode?
The way in which data is transmitted from one device to another device is known as transmission mode. Each communication channel has a direction associated with it, and transmission media provide the direction. Therefore, the transmission mode is also known as a directional mode.

## Slide 58
Simplex-mode Transmission
In Simplex mode, the data flows in one direction. This transmission mode is not very popular as mainly communications require the two-way exchange of data. Keyboard and Monitor are the examples of the simplex mode as a keyboard can only accept the data from the user and monitor can only be used to display the data on the screen. The main advantage of the simplex mode is that the full capacity of the communication channel can be utilized during transmission.

## Slide 59
Half-Duplex Transmission
In a Half-duplex channel the station can transmit and receive the data as well. Messages flow in both the directions, but not at the same time. A Walkie-talkie is an example of the Half-duplex mode. In Walkie-talkie, one party speaks, and another party listens. After a pause, the other speaks and first party listens. The entire bandwidth of the communication channel is utilized in one direction at a time.

## Slide 60
Full-Duplex Transmission
In Full duplex mode, the data flow in both the directions. Both the stations can send and receive the message simultaneously. The Full-duplex mode is the fastest mode of communication between devices. The most common example of the full-duplex mode is a telephone network. When two people are communicating with each other by a telephone line, both can talk and listen at the same time.

## Slide 61: 6.
Digital Transmission

## Slide 62
Digital Transmission ?
Data can be represented either in analog or digital form. The computers used the digital form to store the information. Therefore, the data needs to be converted in digital form so that it can be used by a computer.
Digital-to-digital encoding is the representation of digital information by a digital signal. When binary 1s and 0s generated by the computer are translated into a sequence of voltage pulses that can be propagated over a wire, this process is known as digital-to-digital encoding.
Digital to Digital Conversion ?
three categories

## Slide 63
Unipolar
Digital transmission system sends the voltage pulses over the medium link such as wire or cable. The polarity of each pulse determines whether it is positive or negative. In Unipolar Encoding, '1' is considered as a high voltage and '0' is considered as a zero voltage.

## Slide 64
Polar
Polar encoding is an encoding scheme that uses two voltage levels: one is positive, and another is negative. By using two voltage levels, an average voltage level is reduced, and the DC component problem of unipolar encoding scheme is alleviated.
Polar NRZ
Polar RZ
Polar NRZ
Polar RZ

## Slide 65
Bipolar
If the first 1 bit is represented by positive amplitude, then the second 1 bit is represented by negative voltage, third 1 bit is represented by the positive amplitude and so on. This alternation can also occur even when the 1bits are not consecutive.
AMI (Alternate Mark Inversion) The Binary 0 gets represented by a neutral voltage. On the other hand, alternating negative and positive voltages represent the Binary 1s.
Pseudoternary Here, we encode the bit 1 as a zero voltage, while we encode the bit 0 as alternating negative and positive voltages. It means that this one is exactly the opposite of the AMI scheme. For example, Data = 010010.

## Slide 66: 7.
Transmission Media

## Slide 67
Transmission Media?
Transmission media is a communication channel that carries the information from the sender to the receiver. Data is transmitted through the electromagnetic signals.
Bandwidth :-
The greater the bandwidth of a medium, the higher the data transmission rate of a signal.
Transmission impairment :- When the received signal is not identical to the transmitted one due to the transmission impairment. quality of the signals will get destroyed due to transmission impairment.
Interference :- An interference is defined as the process of disrupting a signal when it travels over a communication medium on the addition of some unwanted signal.
Attenuation means the loss of energy, strength of the signal decreases with increasing the distance
Distortion occurs when there is a change in the shape of signal. This type of distortion is examined from different signals having diff frequencies.
Noise is When data is travelled over a transmission medium, some unwanted signal is added to it

## Slide 68
Classification of Transmission Media?
(Guided Media)
(Unguided Media)

## Slide 69
Guided Media
It is defined as the physical medium in which the signals are transmitted. also known as Bounded media.
Twisted pair
Co-axial
Fibre Optic
STP
UTP

## Slide 70
What is a Cable?
An electrical cable is an assembly of one or more wires running side by side or bundled, which is used to carry electric current. A cable assembly is the composition of one or more electrical cables and their corresponding connectors.

## Slide 71
1. Twisted Pair Cable
Twisted-pair cable is a type of cabling that is used for telephone communications and most modern Ethernet networks. A pair of wires forms a circuit that can transmit data. The pairs are twisted to provide protection against crosstalk, the noise generated by adjacent pairs having RJ-11 & RJ-45 Jacks.
Two Types :-
STP (Shielded Twisted Pair Cable)
UTP (Unshielded Twisted Pair Cable)
Ethernet Port
Connects to a network and high speed Internet upto 100baseT.
Known as RJ-45 Port which use RJ-45 Jack as Interface
This port resides on an Ethernet Card.

## Slide 72
What are RJ connectors?
RJ Connectors are a family of push-and-click connectors for twisted-pair wiring in telephone and network wiring. RJ stands for Registered Jack. RJ types define both a jack or receptacle (female) and a plug (male) type of connector.
The most common types of RJ connectors are as follows:
RJ-11 connector: A 4-wire or 6-wire telephone-type connector
RJ-45 connector: An 8-wire telephone-type connector
RJ-48 connector: An 8-wire telephone-type connector

## Slide 74
2. Patch Cables
Patch cable is often called a straight through cable. In other words, patch cable does not change or swap along its way. Both ends use the same wiring standard: T-568A or T-568B.

## Slide 75
Straight Tip vs Crosstalk

## Slide 76
Patch Cables vs. Crossover Cable: When to Use?

## Slide 77
Scenario 1: PC to PC
Scenario 2: PC to Switch to PC
Scenario 3: PC to Switch to Switch to PC

## Slide 78
3. Coaxial Cable
Coaxial cable is commonly used by cable operators, telephone companies, and internet providers around the world to convey data, video, and voice communications to customers. It has also been used extensively within homes.
BNC Connector
Bayonet Neill–Concelman BNC connector is a series of connectors used for connecting thinnet coaxial cabling to various networking components.

## Slide 80
4. Optic Fibre Cable
Fibre optics is a modern technology used mostly in the telecommunication industry to transmit information digitally as pulses of light through strands of fibre made of glass.Also known as Optical fibres, these strands are about the diameter of a human hair follicle. When bundled into an optical fibre cable, they can transmit data in volumes faster than other mediums over really long distances.
Subscriber Connector SC
This Connector is for structural cabling it is used for high speed
And for single mode fibre cabling
Straight Tip ST
This Connector is for structural cabling it is used for high speed
And for Multi mode fibre cabling

## Slide 83
Unguided Media
They transmits the electromagnetic waves without using physical medium.it is also known as wireless transmission.
Radio Waves
Micro Waves
Infrared Waves
Terrestrial
Satellite

## Slide 84: Radio Waves
Radio waves at lower frequencies can travel through walls whereas higher RF can travel in straight line and bounce back.The power of low frequency waves decreases sharply as they cover long distance. High frequency radio waves have more power. The range in frequencies of radio waves is from 20kHz 300Hz.
.
Applications
television and FM and AM radio broadcasts
military communications
Radio Control Car

## Slide 86: Microwaves
Microwaves travel in straight lines, and so the transmitter and receiver stations should be accurately aligned to each other. Microwaves are unidirectional
Micro waves electromagnetic waves having frequency in the range from 1GHz to 1000 GHz.
Applications
  Cellular phones
  3G, 4G or 5G Network
  Satellites
  Wireless LAN
  Wireless PAN

## Slide 88: Infrared
Infrared waves are those between the frequencies 300GHz and 400THz in the electromagnetic spectrum. Their wavelengths are shorter than microwaves but longer than visible light. Infrared propagation is line of sight. Range lies bwtween 300 GHz to 400 THz.
Applications
Remote controls for television, stereos and other appliances.
Wireless modem, keyboard, mouse, printer etc
Night vision systems
Motion detectors
MRI

## Slide 90: 8.
How Internet Works

## Slide 92
1. Satellite

## Slide 93
2. Submarine Cables

## Slide 94: 9.
IP Addressing IPv4 & IPv6

## Slide 95
An Internet Protocol address is a numerical label assigned to each device connected to a computer network that uses the Internet Protocol for communication. An IP address serves two main functions: host or network interface identification and location addressing.
What is IP Address?

## Slide 96: IP Addressing IPv4
An IP address basically a 32-bit address that uniquely universally defines connection of host or a router to the Internet. IP address is unique.
Introduced by IANA (Internet Assigned Numbers Authority).
32 bit is divided into 4 equal parts of 8-8 bits separated by dotted decimal notation. It is in the range of minimum 0.0.0.0 to 255.255.255.255.
Each 8 bit group is known by OCTET.

## Slide 97: Various IP classes
IP has five different classes differentiated by characteristics.
Class-A ranges from 0 to 127
Class-B ranges from 128 to 191
Class-C ranges from 192 to 223
Class-D ranges from 224 to 239
Class-E ranges from 240 to 255
First Octet is defines the class of particular IP e.g. - 128.11.3.31 is follow in class –B
127.0.0.0 to 127.255.255.255 is a range of look back IP.

## Slide 98
Class-A
Class A addresses only include IP starting from 1.x.x.x to 126.x.x.x only. The IP range 127.x.x.x is reserved for loopback IP addresses.
The default subnet mask for Class A IP address is 255.0.0.0 which implies that Class A addressing can have 126 networks (27-2) and 16777214 hosts (224-2).

## Slide 99
Class B
Class B IP Addresses range from 128.0.x.x to 191.255.x.x. The default subnet mask for Class B is 255.255.x.x.
Class B has 16384 (214) Network addresses and 65534 (216-2) Host addresses.

## Slide 100
Class C
Class C IP addresses range from 192.0.0.x to 223.255.255.x. The default subnet mask for Class C is 255.255.255.x. Class C gives 2097152 (221) Network addresses and 254 (28-2) Host addresses.

## Slide 101
Class-D
Class D has IP address range from 224.0.0.0 to 239.255.255.255. Class D is reserved for Multicasting. In multicasting data is not destined for a particular host, that is why there is no need to extract host address from the IP address, and Class D does not have any subnet mask.

## Slide 102
Class-E
This IP Class is reserved for experimental purposes only for R&D or Study. IP addresses in this class ranges from 240.0.0.0 to 255.255.255.254. Like Class D, this class too is not equipped with any subnet mask.

## Slide 103
255
255
255
255
Dotted Decimal
Maximum
Network
Host
32 bits
IP Addressing
Notes: Layer 1 of 3:
Purpose: This figure show the general format of an IP address.
In layer 1, the address is 32 bits with a network and host portion.

## Slide 104: IP Addressing
255
255
255
255
Dotted Decimal
Maximum
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
Binary
32 bits
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
IP Addressing
Notes: Layer 3 of 3:
In layer 2, one can convert the address to binary.

## Slide 105: IP Addressing
255
255
255
255
Dotted Decimal
Maximum
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
10101100
00010000
01111010
11001100
Binary
32 bits
172
16
122
204
Example Decimal
Example Binary
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
IP Addressing
Notes: Layer 3 of 3:
In layer 3, an example of dotted-decimal format and binary are displayed.
Emphasize: IP address format is dotted-decimal. Dotted-decimal makes it easy to work with IP addresses. However, in this course we will work with the addresses on the bit level, so we will convert these addresses into binary, make changes to them, and convert them back.
The central authority for addresses is the Internet Assigned Numbers Authority.
Note: This most common form of addressing reflects the widely used IP version 4. Faced with the problem of depleting available addresses, Internet Engineering Task Force (IETF) work is under way for a backward-compatible next generation of IP (IPng, also called IP 6).
IP 6 will offer expanded routing and addressing capabilities with 128-bit addresses rather than the 32-bit addressing shown on the graphic. Addresses from both IP versions will coexist. Initial occurrences will probably be at locations with address translator software and firewalls.

## Slide 106
Class A:
Class B:
Class C:
Class D: Multicast
Class E: Research
Network
Host
Host
Host
Network
Network
Host
Host
Network
Network
Network
Host
8 bits
8 bits
8 bits
8 bits
IP Address Classes
Notes: Purpose: This graphic describes the three most common classes of IP address.
Emphasize: Discuss classes of addresses. Each address contains information about the network number and the host number of the device. Class A addresses are for very large organizations. Class B addresses are for smaller organizations, and Class C addresses for even smaller ones.
As the number of networks grows, classes may eventually be replaced by another addressing mechanism, such as classless interdomain routing (CIDR). RFC 1467, Status of CIDR Deployment in the Internet, presents information about CIDR. RFC 1817, CIDR and Classful Routing, also presents CIDR information.

## Slide 107: IP Address Classes
1
Class A:
Bits:
NNNNN
Host
Host
Host
8
9
16
17
24
25
32
Range (1-126)
1
Class B:
Bits:
NNNNNN
Network
Host
Host
8
9
16
17
24
25
32
Range (128-191)
1
Class C:
Bits:
NNNNNN
Network
Network
Host
8
9
16
17
24
25
32
Range (192-223)
1
Class D:
Bits:
NNNNNN
Multicast Group
Multicast Group
Multicast Group
8
9
16
17
24
25
32
Range (224-239)
IP Address Classes
Notes: Emphasize: Highlight the fixed values that start each class address.
The first octet rule states that when an address falls into a specified range, it belongs to a certain class. Students should soon be able to recognize the address class of any IP address on sight.
Note: If time or interest permits, you can use the initial bit patterns in the first octet and show how a class of IP network derives the range of network numbers for that IP address class.

## Slide 108
11111111
172 16 0 0
10101100
00010000
00000000
00000000
16 15 14 13 12 11 10 9
8 7 6 5 4 3 2 1
Network
Host
00000000
00000001
11111111
11111111
11111111
11111110
...
...
00000000
00000011
11111101
1
2
3
65534
65535
65536
-
...
2
65534
N
2N-2 = 216-2 = 65534
Determining Available Host Addresses
Notes: Purpose: This figure explains how to calculate the number of available hosts in a network.
Emphasize: 2N-2 is the calculation to determine available hosts. N is the number of binary digits in the host field. Subtract 2 because a host cannot be all 0s or 1s.
The same principal applies when determining the number of available networks.

## Slide 109
172
16
0
0
255
255
0
0
255
255
255
0
IP Address
Default Subnet Mask
8-bit Subnet Mask
Network
Host
Network
Host
Network
Subnet
Host
Also written as “/16” where 16 represents the number of 1s in the mask.
Also written as “/24” where 24 represents the number of 1s in the mask.
11111111
11111111
00000000
00000000
Subnet Mask
Notes: Emphasize: Turn on more bits to represent subnets.
Compare the default or standard subnet mask with the subnet mask in the slide.
These are the rules for IP addressing:
  An address is 32 bits, divided into three components:
    First octet rule bits
    Network bits (path selection bits)
    Node bits
  The first octet rule states that the most significant bit pattern in the first octet determines the class of the address.
  Path selection bits cannot be all ones or zeros.
  Certain addresses are reserved. RFC 1918 defines some of those.
  Prefix or mask one bits are path selection significant; zero bits are host bits and therefore not significant.
  Use the logical AND to combine the address and mask bits to get the subnet address.
  The maximum number of available subnets equals 2 prefix bits - 2; the maximum number of available hosts equals 2 32- prefix bits - 2.

## Slide 110
16
Network
Host
172
0
0
10101100
11111111
10101100
00010000
11111111
00010000
00000000
00000000
10100000
00000000
00000000
00000010
172.16.2.160
255.255.0.0
Network Number
Subnet Mask without Subnets
Notes: Purpose: This graphic explains how routers use addresses that have no subnet mask.
Emphasize: Explain how masking works at the bit level. Zero bits mask host information.
Note: This is an easy place to lose students. At this point, they need to learn several abstract mathematical concepts before we can show them how to lay out an IP-addressed network. To the novice these techniques may seem unrelated, making the presentation confusing. To a more experienced audience, these techniques will be familiar.

## Slide 111
16
Network
Host
172.16.2.160
255.255.255.0
172
2
0
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
00000000
00000000
00000010
Subnet
Network Number
Subnet Mask with Subnets
Notes: Purpose: This figure shows how the router determines an address when subnetting is used.
Emphasize: This example makes a Class B address space look like a collection of Class C address spaces.
Now the logical AND allows us to extract the subnet number as well as the assigned network number.
An exercise follows that tests the students’ understanding of subnet masks.

## Slide 112: IP Addressing IPv6
An IP address basically a 128-bit address that uniquely universally defines connection of host or a router to the Internet. IP address is unique.
Introduced by IANA (Internet Assigned Numbers Authority).
total of 4,294,967,296 unique IP addresses can be assigned to hosts.
IP is like 2001:db8:1234::f350:2256:f3dd/64
It supports Unicast. Telecast & Multicast.
It doesn’t have Classes like ipv4

## Slide 114: 10.
Subnet Mask, MAC, DHCP & DNS

## Slide 115
What is Subnet Mask?
A subnet mask is a 32-bit number that segments an existing IP address in a TCP/IP network. It is used by the TCP/IP protocol to determine whether a host is on the local subnet or on a remote network. Subnet mask divides the IP address into a network address and host address, hence to identify which part of IP address is reserved for the network and which part is available for host use.

## Slide 117: MAC Address
The Media Access Control (MAC) address is just as important as the IP address. The MAC address is a unique value associated with the network adapter (NIC). MAC addresses are known as the hardware addresses or physical addresses. They uniquely identify the adapter on the LAN.

## Slide 118
MAC Address

## Slide 119: DHCP
Dynamic Host Configuration Protocol (DHCP)
  From 1993
  An extension of BOOTP, very similar to DHCP
  Same port numbers as BOOTP
  Extensions:
    Supports temporary allocation (“leases”) of IP addresses
    DHCP client can acquire all IP configuration parameters needed to operate
  DHCP is the preferred mechanism for dynamic assignment of IP addresses
  DHCP can interoperate with BOOTP clients.

## Slide 121: DHCP Interaction

## Slide 122
APIPA stands for Automatic Private IP Addressing (APIPA). It is a feature or characteristic in operating systems (eg. Windows) which enables computers to self-configure an IP address and subnet mask automatically when their DHCP(Dynamic Host Configuration Protocol) server isn't reachable
APIPA

## Slide 123: DNS
DNS stands for Domain Name System. DNS is a service that translates the domain name into IP addresses. This allows the users of networks to utilize user-friendly names when looking for other hosts instead of remembering the IP addresses.
(The format of country domain is same as a generic domain)
(It defines the registered hosts according to their generic behavior.)
(The inverse domain is used for mapping an address to a name.)

## Slide 124
Importance of DNS

## Slide 125: 11.
WLAN & WPAN Networks

## Slide 126: WLAN
A wireless LAN is a wireless computer network that links two or more devices using wireless communication to form a local area network within a limited area such as a home, school, computer laboratory, campus, or office building.
Wi-Fi
 What is Wi-Fi
 Short for “Wireless Fidelity”
 A trademark of the Wi-Fi Alliance
 The brand name for products using the IEEE 802.11 family of standards
 Commonly used for “wireless local area network” (WLAN)

## Slide 128: WPAN
A personal area network is a computer network for interconnecting electronic devices within an individual person's workspace. A WPAN provides data transmission among devices such as computers, smartphones, tablets and personal digital assistants.
 Wireless Personal Area Networks (WPAN)
 Design goal
 Cable replacement
 Low cost
 Low power
 Small size
 For mobile devices
Bluetooth

## Slide 130: 12.
OSI Model

## Slide 131: INTRODUCTION
The OSI Model (Open Systems Interconnection Model) is a conceptual framework used to describe the functions of a networking system. The OSI model characterizes computing functions into a universal set of rules and requirements in order to support interoperability between different products and software.

## Slide 132: OSI MODEL

## Slide 133: Data, Protocol & Activities
TCP/IP Suit
OSI Layers
Application
Telnet, FTP, SMTP, HTTP, DNS, SNMP, Specific address etc…
Transport
SCTP, TCP, UDP, Sockets and Ports address
Network
IP, ARP/RARP, ICMP, IGMP
Data Link
IEEE 802 Standards, PPP, Physical address
Application
Session
Presentation
Transport
Network
Data Link
Activities
To Accessing or transfering the data.
To establish, manage, and terminate session
To Translate, encrypt, and compress data
To Provide reliable process-to-process Message delivery and error recovery
To move packets from source to destination; to provide internetworking
To organize bits into frames; to provide Hop-to-hop delivery
Physical
Medium, Coax, Fiber, 10base, Wireless
Physical
To Transmit bits over a medium; to provide Mechanical and electrical specifications
Presentation
SSL, TLS, NDR
Session
API,PPTP, PAP, ASP, L2F, L2TP, SMPP

## Slide 134: PHYSICAL LAYER





Physical characteristics of interface and medium (Transmission medium)
Representation of bits (stream of bits (0s or 1s) with no interpretation and encoded into signals)
Line configuration (Point-to-Point, Point-to-Multipoint)
Physical topology
Transmission mode (Simplex, half duplex, full duplex)
110 | 10101000000010111
From data link layer
110 | 10101000000010111
To data link layer
Physical layer
Physical layer
Transmission medium

## Slide 135

Data link layer is responsible for moving frames from one hop (Node) to the next.

Concerned:





Framing (stream of bits into manageable data units) Physical addressing (MAC Address)
Flow Control (mechanism for overwhelming the receiver) Error Control (trailer, retransmission)
Access Control (defining master device in the same link)
Data
H2
T2
From network layer
Data
H2
T2
To network layer
To physical layer
From physical layer
Data link layer
Data link layer
DATALINK Layer

## Slide 136: NETWORK LAYER

The network layer is responsible for the delivery of individual packets from the source host to the destination host.

Concerned:


Logical addressing (IP Address)
Routing (Source to destination transmission between networks)
Data
H3
Packet
From transport layer
To data link layer
Data
H3
Packet
To transport layer
From data link layer
Network layer
Network layer

## Slide 137

The transport layer is responsible for the delivery of a message from one process to another

Concerned:



Service-point addressing (Port address)
Sequence Number (data reassembly)
Segmentation and reassembly (Sequence number)
Segments
H4 | Data |  | H4 | Data
From session layer
To network layer
Transport layer
H4 | Data
Segments
H4 | Data
From session layer
From network layer
Transport layer
H4 | Data
H4 | Data
TRANSPORT LAYER

## Slide 138: SESSION LAYER

The session layer is responsible for authentication & authorization.

Concerned:


Session establishment (Starts & terminates sessions)
Dialog Control (allows to communicate 2 systems in Half Duplex/Full duplex)
Synchronization (checks error in fixed time interval to avoid errors)
Data
H5
From Presentation layer
To transport layer
Data
Data
Syn
Syn
Syn
Data
H5
To Presentation layer
From transport layer
Data
Data
Syn
Syn
Syn
Session layer
Session layer


## Slide 139: PRESENTATION LAYER

The presentation layer is responsible for translation, compression and encryption

Concerned:



Translation (interoperability between different encoding system) Encryption (Privacy schemes)
Compression (data compression)
Data
H6
From application layer
To session layer
Data
H6
To application layer
From session layer
presentation layer
presentation layer

## Slide 140
Data
H7
USER
(Human or Program)
To presentation layer
Data
H7
Application layer
Application layer
Message
Message

The application layer is responsible for providing services to the user.

Concerned:



Web surfing protocols
File transfer, access and management Mail services
X.500
FTAM
X.400
X.500
FTAM
X.400
From presentation layer
USER
(Human or Program)
APPLICATION Layer

## Slide 141: 13.
TCP/IP Model

## Slide 142
Model

## Slide 143: Network Access Layer
A network layer is the lowest layer of the TCP/IP model.
A network layer is the combination of the Physical layer and Data Link layer defined in the OSI reference model.
It defines how the data should be sent physically through the network.
This layer is mainly responsible for the transmission of the data between two devices on the same network.
The functions carried out by this layer are encapsulating the IP datagram into frames transmitted by the network and mapping of IP addresses into physical addresses.
The protocols used by this layer are ethernet & token ring

## Slide 144: Internet or Network Layer
An internet layer is the second layer of the TCP/IP model.
An internet layer is also known as the network layer.
The main responsibility of the internet layer is to send the packets from any network, and they arrive at the destination irrespective of the route they take.
IP Addressing
Host-to-host communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
ARP Protocol

## Slide 145: Transport Layer
The transport layer is responsible for the reliability, flow control, and correction of data which is being sent over the network.
The two protocols used in the transport layer are User Datagram protocol and Transmission control protocol.
TCP & UDP

## Slide 146: Application Layer
An application layer is the topmost layer in the TCP/IP model.
It is responsible for handling high-level protocols, issues of representation.
This layer allows the user to interact with the application.
When one application layer protocol wants to communicate with another application layer, it forwards its data to the transport layer.
HTTP
SNMP
SMTP
HTTPS
DNS
TELNET
FTP

## Slide 147: 14.
TCP UDP

## Slide 149
TCP vs UDP

## Slide 150
TCP UDP Port Numbers of
Internet Protocols Suite

## Slide 151: 15.
ARP & RARP

## Slide 152: Why We Use ARP?
Used to convert an IP address into a physical address such as an Ethernet address.A host wishing to obtain a physical address broadcasting ARP request onto the TCP/IP network.

## Slide 154: Why We Use RARP
The Reverse Address Resolution Protocol (RARP) is an obsolete computer networking protocol used by a client computer to request its Internet Protocol (IPv4) address from a computer network.
Reverse Address Resolution Protocol (RARP) is a network layer protocol used to resolve an IP address from a given hardware address (such as an Ethernet address).

## Slide 156: 16.
CSMA/CA & CSMA/CD

## Slide 157
Carrier Sense Multiple Access (CSMA)
This method was developed to decrease the chances of collisions when two or more stations start sending their signals over the datalink layer. Carrier Sense multiple access requires that each station first check the state of the medium before sending.
CSMA/CD
CSMA/CA

## Slide 159
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
Carrier Sense Multiple Access/with Collision Avoidance (CSMA/CA) is a network contention protocol used for carrier transmission in networks using the 802.11 standard. In contrast to the Carrier Sense Multiple Access/Collision Detect (CSMA/CD) protocol, which handles transmissions only after a collision has taken place, CSMA/CA works to avoid collisions prior to their occurrence. CSMA/CA increases network traffic as it requires sending out a signal to the network even before transmitting any real data. This is to listen for any collision scenarios in the network and to inform other devices not to transmit.

## Slide 160
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Carrier Sense Multiple Access with Collision Detection (CSMA/CD) is a network protocol for carrier transmission that operates in the Medium Access Control (MAC) layer. It senses or listens whether the shared channel for transmission is busy or not, and defers transmissions until the channel is free. The collision detection technology detects collisions by sensing transmissions from other stations. On detection of a collision, the station stops transmitting, sends a jam signal, and then waits for a random time interval before retransmission

## Slide 161: 17.
PROXY & VPN

## Slide 162: PROXY
If you are wanting to surf the web anonymously then proxies can provide you with a means to hide your home IP address from the rest of the world. By connecting to the internet through proxies, the home IP address of your machine will not be shown but rather the IP of the proxy server will be shown.
PROXY SERVER
A proxy server is a server application that acts as an intermediary between a client requesting a resource and the server providing that resource.

## Slide 163: What is a VPN ?
A VPN is a service that both encrypts your data and hides your IP address by bouncing your network activity through a secure chain to another server miles away. This obscures your online identity, even on public Wi-Fi networks, so you can browse the internet safely, securely and anonymously.

## Slide 164
Intranet VPNs - If a company has one or more remote locations that they wish to join in a single private network, they can create an intranet VPN to connect LAN to LAN.
Remote Access VPN :- A remote access virtual private network (VPN) enables users who are working remotely to securely access and use applications and data that reside in the corporate data center and headquarters, encrypting all traffic the users send and receive.
1.
2.

## Slide 165
Extranet VPNs – An extranet VPN links outside customers, suppliers, partners, or communities of interest to an enterprise customer's network over a shared infrastructure using dedicated connections
3.

## Slide 166: 18.
Server & Datacenter

## Slide 167
A server is a computer or system that provides resources, data, services, or programs to other computers, known as clients, over a network. In theory, whenever computers share resources with client machines they are considered servers. ... This means that a device could be both a server and a client at the same time.
What is a Server?

## Slide 168
A COMPUTER (HARDWARE)?
A PROGRAM (SOFTWARE)?
OR
WHAT IS A SERVER?

## Slide 169
A COMPUTER (HARDWARE)?
A PROGRAM (SOFTWARE)?
OR
WHAT IS A SERVER?

## Slide 170
A typical PC (Desktop or Laptop)
+
Apache HTTP Server (Software)
=
Web Server
WHAT IS A SERVER?

## Slide 171: REQUEST
REQUEST
REQUEST
How Server Works?

## Slide 172: SERVICE
SERVICE
SERVICE
How Server Works?

## Slide 173
Type | Provide… | Examples
Database Server | Database Services | Microsoft SQL Server Oracle Database MySQL
Web Server | Web Sites Hosting | Apache HTTP Server Microsoft IIS (Part of Microsoft Windows)
File Server | File Services (Storing Shared Files) | Microsoft Windows Storage Server (Built on the Microsoft Windows Server)
Server Types?

## Slide 174
Type | Provide… | Examples
Mail Server | E-mail Services | Microsoft Exchange Server IBM Lotus Domino
Application Server | An Environment To Run Certain Applications | Oracle WebLogic Server Oracle Application Server Oracle GlassFish Server Zend Server
DNS Server | Translation of Domain Names Into IP Addresses | Microsoft Windows Server BIND
Server Types?

## Slide 175
Type | Provide… | Examples
Proxy Server | Filtering And Caching | Microsoft Forefront Threat Management Gateway (ISA Server) Apache HTTP Server Apache Traffic Server
Print Server | Printer Services | Microsoft Windows Storage Server (Built on the Microsoft Windows Server)
OTHER TYPES OF SERVERS:
FTP Server, Chat Server, Fax Server, Game Server, Audio/Video Server
Server Types?

## Slide 176
A backup server is a type of server that facilitates data, file, application, and/or database backup. It has both hardware and software capabilities so you can manage and recover your backups – it can be locally-based or a remote backup server. ... When it comes to cloud deployment, a remote backup server is used.
Backup Server
Exchange Server
Microsoft Exchange Server is Microsoft's email, calendaring, contact, scheduling and collaboration platform. It is deployed on the Windows Server operating system (OS) for business use. Microsoft designed Exchange Server to give users access to the messaging platform from mobile devices, desktops and web-based systems. Telephony capabilities in Exchange Server support voice messages.

## Slide 178: WHAT IS A DATA CENTER
 Data centers are designed to house information systems and related components such as:
 Servers
 Routers
 Storage
 Uninterruptable power
supplies (UPS)
 Cooling Units
 Data centers have unique and typically large power requirements
 They are often raised floor designs to accommodate the large amount of cables required.

## Slide 179: DATA CENTER COMPONENTS: COOLING
 Approximately half of the power consumed in the data center is used in cooling
 Cooling Options
 Computer Room Air Conditioning (CRAC)
 Liquid Cooling
 Air Side Economizers
DATA CENTER COMPONENTS: UPS
 Uninterruptable Power Supply (UPS)
 Conditions power
 Provides power to avoid outages during power failure lasting seconds or minutes
 Provides time to shutdown, failover, or initiate backup power for longer outages

## Slide 181: 19.
Network Security

## Slide 182
Computer network security consists of measures taken by business or some organizations to monitor and prevent unauthorized access from the outside attackers.
Computer Network Security
Privacy :-
Message Integrity :-
Authentication :-
Non Repudiation :-
The transmitted message should be sent only to the intended receiver while the message should be opaque for others.
Data integrity means that the data must arrive at the receiver exactly as it was sent. There must be no changes in the data content during transmission
Authentication means that the receiver is sure of the senders identity, i.e., no imposter has sent the message.
Non-Repudiation means that the receiver must be able to prove that the received message has come from a specific sender.

## Slide 183
Encryption/Decryption
Encryption: Encryption means that the sender converts the original information into another form and sends the unintelligible message over the network.
Decryption: Decryption reverses the Encryption process in order to transform the message back to the original form.
The data which is to be encrypted at the sender site is known as plaintext, and the encrypted data is known as ciphertext. The data is decrypted at the receiver site.
There are two types of Encryption/Decryption techniques:
Privacy with secret key Encryption/Decryption
Privacy with public key Encryption/Decryption
Algorithms :- DES, 3DES, AES & RCA, RSA

## Slide 184
Secret Key Encryption/Decryption technique
Public Key Encryption/Decryption technique
In Secret Key Encryption/Decryption technique, the same key is used by both the parties, i.e., the sender and receiver.
There are two keys in public key encryption: a private key and a public key.The private key is given to the receiver while the public key is provided to the public.

## Slide 185: 20.
NAS & NAT

## Slide 186
Network-attached storage (NAS) is dedicated file storage that enables multiple users and heterogeneous client devices to retrieve data from centralized disk capacity. Users on a local area network (LAN) access the shared storage via a standard Ethernet connection.
Network Attached Storage (NAS)

## Slide 187: Network Address Translation (NAT)
To access the Internet, one public IP address is needed, but we can use a private IP address in our private network. The idea of NAT is to allow multiple devices to access the Internet through a single public address. Network Address Translation (NAT) is a process in which one or more local IP address is translated into one or more Global IP address
Uses private addresses:
    10.0.0.0-10.255.255.255,
    172.16.0.0-172.32.255.255 or
    192.168.0.0-192.168.255.255

## Slide 188: Network Address Translation (NAT)
There are 3 ways to configure NAT:
Static NAT :-
Dynamic NAT :-
Port Address Translation (PAT) :-
A static network address translation (static NAT) is a type of NAT technique that routes and maps network traffic from a static public IP address to an internal private IP address and/or network.
Dynamic network address translation (Dynamic NAT) is a technique in which multiple public Internet Protocol (IP) addresses are mapped and used with an internal or private IP address.
Port address translation (PAT) is a function that allows multiple users within a private network to make use of a minimal number of IP addresses. Its basic function is to share a single IP public address between multiple clients who need to use the Internet publicly. It is an extension of network address translation (NAT).

## Slide 189: Basic Operation of NAT

## Slide 190: 21.
RAID (Redundant Array of Independent Disk)

## Slide 191: RAID : Redundant Array of Independent Disk
RAID, or “Redundant Arrays of Independent Disks” is a technique which makes use of a combination of multiple disks instead of using a single disk for increased performance, data redundancy or both.

## Slide 192: RAID 1(Mirrored)
strip 0
strip 4
strip 8
strip 12
strip 1
strip 5
strip 9
strip 13
strip 2
strip 6
strip 10
strip 14
strip 3
strip 7
strip 11
strip 15
strip 0
strip 4
strip 8
strip 12
strip 1
strip 5
strip 9
strip 13
strip 2
strip 6
strip 10
strip 14
strip 3
strip 7
strip 11
strip 15

## Slide 198: 22.
Sharing Folder in Network

## Slide 199
Permissions
Discovery of Network
Sharing Privacy
Firewall Rule
Same Network
For Sharing…

## Slide 200: 23.
Telnet in Network

## Slide 201: Telnet Remote Config?
Telnet utility allows users to test connectivity to remote machines and issue commands through the use of a keyboard.
Network Virtual Terminal
Network Virtual terminal: An application layer allows a user to log on to a remote host.

## Slide 202: 24.
Remote Desktop Connection

## Slide 203
Remote Desktop Connection (RDC) is a technology that permits a computer to connect, gain access and take control of a remote PC over a network. It implements Remote Desktop Protocol (RDP) through Terminal service or Windows Remote Desktop Service to gain remote access over a computer or a network.
Remote Desktop Connection

## Slide 204: 25.
Windows Remote Assistance

## Slide 205
A remote assistance when enabled allows another user on the Internet to use your computer. This may be asked by Microsoft agent or your friend or something else. Take caution while giving anyone remote access, this means everything in the PC is accessible to the one who has taken control.
Windows Remote Assistance

## Slide 206: 26.
FTP in Network

## Slide 207
A popular means of data exchange is connecting computers to one another. The File Transfer Protocol (FTP) is used to transfer files between two computers over a network and Internet. ... Auto FTP Manager is an advanced FTP client that automates file transfers between your computer and the FTP server.
FTP (File Transfer Protocol)

## Slide 208: 27.
Configuring Network

## Slide 209
Let’s Configure Network

## Slide 210: 28.
Configuring Router

## Slide 211
Let’s Configure Router

## Slide 212: 29.
Protocols You need to know

## Slide 213
Protocols
IP
HTTP
HTTPS
FTP
TFTP
SMTP
POP3
IMAP
SNMP
TELNET
ICMP
IGMP

## Slide 214: 30.
Networking Commands One should know

## Slide 215
Commands
Ipconfig
systeminfo
Hostname
Ping
getmac
Tracert
Netstat
Nslookup
Netsh wlan show profiles
Netsh wlan show all
Netsh wlan show interfaces
Netsh wlan export profile name
Netsh wlan add profile name
Netsh wlan delete profile name

## Slide 216
Thank You